## Slide 1: Planning
12. Purchasing and supply chain management
Notes: <number>

## Slide 2: Program
Purchasing and supply chain management: definitions
Materials requirements planning
Basic logistics structures
Just-in-time management (JIT)
Consequences for suppliers
Scheduling problems between purchasing and logistics
Elements of the purchasing system

## Slide 3: Purchasing and Supply Chain Management: definitions
Marketing
Manufact.
& logistics
Purchasing
1st Tier
Supplier
2nd Tier
Supplier
Customer
Value Chain Management
Demand Chain Management
Supply Chain Management
Business Logistics
Physical Distribution
Materials management
Logistics management

## Slide 4: Purchasing and Supply Chain Management: definitions
Materials management encompasses all materials related activities aimed at optimizing the incoming materials flow from the supplier to production.
Logistics management encompasses all materials flows, from the flows of purchased materials into a facility, through the manufacturing process, and out to the customer.
Supply Chain Management (SCM) is a connected series of activities which is concerned with planning, coordinating and controlling material, parts, and finished goods from suppliers up to the customer.
Purchasing and Supply management can be seen as an integrated part of SCM

## Slide 5: Materials requirements planning
MRP starts in the sales department with drawing up a sales plan, providing an estimate of the volume to be sold. MRP is the input for the manufacturing planning and control system consisting of:
  Master planning Plans at the level of the product families (product groups) are established. Customer orders, sales plan, planned stocks of finished products and the production and purchasing plans are linked together
  Manufacturing Resources Planning (MRP-II) Records the Manufacturing Resources needed to realize the master plan.

## Slide 6: Materials requirements planning
Master production scheduling (MPS) Translates the master plan into specific materials requirements. MPS provides the input for calculating the net materials requirements.
General capacity testing The MPS should be tested for capacity limitations and this should be done for all potential bottleneck capacities.
Materials requirement planning (MRP-I) The materials requirements planning explodes the requirements from the MPS level on a weekly basis, step by step, in accordance with the bill of materials.
Capacity requirements planning Conceptually comparable with materials requirements planning. The current and planned manufacturing orders from the mrp provide the input for the detailed production line planning

## Slide 7: Materials requirements planning
Order release Order releases change the status of the manufacturing orders from ‘planned’ to ‘released’. The decision to release is based on the availability of the required materials and capacity.
Priority management The priorities are directly derived from the MPS. Each unit receives a priority sheet which lists all manufacturing orders for that line or machine center.
Capacity Management Waiting times per processing group have to be controlled. Input/output reports have an important function: to compare the realized output for a production unit against its planned output.

## Slide 8
Resource
Planning
Production
Planning
Master production
scheduling
Demand
management
Front end
Material requirements
planning
Time-phased
requirements record
Materials and
capacity plans
Purchasing
Vendor follow-up
systems
Rough-cut
capacity planning
Routing
file
Bills of
Materials
Inventory
status
data
Detailed
capacity
planning
order
release
Shop-floor control
Engine
Back
end
Manufacturing
planning and
control system

## Slide 9: Materials requirements planning
Difference MRP-I and MRP-II
MRP-I stands for materials requirements planning; aims at releasing and managing manufacturing orders and purchasing requisitions.
MRP-II stands for manufacturing resources planning, an integrated system that controls relevant materials flows and production capacity while also taking into account the relationship between these materials flows and the required capacity.

## Slide 10: Basic logistics structures
Order decoupling point (or order penetration point):
  Indicates how deeply the customer order penetrates the firm’s materials planning systems
  Defines from what moment on a production order becomes customer specific.

## Slide 11: Basic logistics structures
Five basic manufacturing and logistics structures
Making and sending to stock (MSS) | Products are manufactured and distributed to distribution points which are dispersed and located close to the customer. E.g. sweets, foods, beverages.
Making to (central) stock (central stock | Finished products are kept in stock at the end of the production process and are from there shipped to geographically dispersed customers. E.g. dairy products.
Assembly to order (ATO) | Only systems elements, modules or subassemblies are in stock at the manufacturing center, whereas final assembly takes place based on a specific customer order. E.g. cars, computers.
Making to order (MTO) | Only raw materials and components are kept in stock. Every customer is a specific project. E.g. beer and lemonade cans, basic construction materials
Engineering and making to order (ETO) | No stock at all. The purchase and order of materials takes place based on the specific customer order. E.g. construction companies and shipyards.

## Slide 12: The order decoupling point concept
Supplier
IG
Components WIP Assembly
Manufacturing
EP
Installation
EP
Customer
OP1
Production
Sales/marketing
Examples
Kitchen
appliances
Computer
systems
High-end
furniture
Ship propelling
diesel engines
Shipbuilding
Make and send to stock (MSS)
OP2
Make to stock (MTS)
OP3
Assemble to order (ATO)
Forecast based, i.e.
planning based
activities
OP4
Make to order (MTO)
OP5
Engineer and make to order (ETO)
Customer driven
activities
IG= Incoming goods
EP= End products
WIP= Work in Progress
OP= Order pentration point
= Inventory
=Order driven
=forecast driven
(Hoekstra and Romme, 1985)

## Slide 13: Just-in-time management (JIT)
Characteristics of JIT management:
JIT
All materials and products become available at the very moment when they are needed in the production process, not sooner and not later but exactly on time and exactly in the right quantity.
Major objective
Continuously tackle and solve manufacturing bottlenecks within, and interfaces between, consecutive steps in the manufacturing process.

## Slide 14: Just-in-time management (JIT)
Order Quantities and batch sizes
Economic Order Quantity: where the sum of inventory costs
and ordering costs is lowest
Camp’s formula: Qo= √ ((2S x Co)/Ci)
S= fixed usage per period
Q= order quantity
Co= costs per order
Ci= inventory carrying costs for one unit during one unit time

## Slide 15: Just-in-time management (JIT)
Conditions Camp’s formula:
The consumption of the component at hand is fairly stable
The consumption of the component is evenly spread over the course of time
The delivery time of the product is fixed and not due to fluctuation
the ordering costs per order are fixed
the inventory carrying costs do not depend on the ordered quantity
JIT basically challenges each of these assumptions. E.g.
order-related costs are analyzed in terms of costs related to:
Negotiations with the supplier
Administrative processing
Follow-up and expediting of orders
Incoming and quality inspections

## Slide 16
Towards a reduction of
the economic order quantity
Just-in-time management (JIT)

## Slide 17: Just-in-time management (JIT)
JIT production and scheduling cannot successfully implemented without a zero defects philosophy
JIT and zero defects need to go hand-in-hand:
  Smaller batches make it necessary to detect quality defects at an early stage
  JIT must be supported by all functions within the company
  Adopting JIT will take time (It took Toyota 15 years to implement he KANBAN philosophy)

## Slide 18
Just-in-time management (JIT)
Purchasing activity | Traditional approach | JIT approach
Supplier selection | Minimum of 2 suppliers; price is central | Often one local supplier; frequent deliveries
Change of orders | Delivery time and quality often changed at the last moment | Delivery time and quality fixed; quantities are adjusted within predetermined margins if necessary
Follow-up orders | Many phone calls to solve delivery problems | Few delivery problems thanks to sound agreements; quality and delivery problems are not tolerated
Incoming inspection | Inspection of quality and quantities of nearly every delivered order | Initial sample inspections; later, no inspections necessary
Supplier assessment | Qualitative assessment; delivery deviations of sometimes up to 10% are tolerated | Deviations are not accepted; price is fixed based on open calculation
Invoicing | Payment per order | Invoices are collected and settled on a monthly basis
JIT and the purchasing function

## Slide 19: Consequences for suppliers
Advantages of JIT for a supplier
  Supplier is able to plan his production volume much better because he’s informed regularly about the quantities to be delivered.
  Administrative savings: supplier’s and customer’s production and materials planning systems are linked through electronic information systems (like EDI),
  Constant communication on quality and costs improvements can lead to product and process innovation
  Investment policy: JIT contracts are signed for a long period of time and guarantee a certain volume and turnover over that time period

## Slide 20
Disadvantages of JIT for a supplier
  It may result in a pyramid shaped structure with a strong hierarchy in the different links of the supply chain. The large manufacturers at the top of the pyramid impose their demands ruthlessly on the often smaller first tier suppliers
  It takes time (and money) to deliver at zero defects or to produce zero defects. These investments come at the expense of the supplier
  Supplier can become very dependent on only one manufacturer. This can become a threat to its continuity.
Consequences for suppliers

## Slide 21
‘A’ Company
Finished car prod
In-house In house
assembly. Manufactt
The first supplier
Capital involvement
of company ‘A’ in38
supplying companies
118 supplying
companies for
company ‘A’
Function parts, mounting parts for inside and
outside mechanical reworking, press reworking
The secondary supplier
2000-3000 companies
Press, gilding cutting, screw, casting, specials parts reworking
other secondary
suppliers
500-600
companies
Tooling, mould,
fittings
The other third suppliers
7000-10000 companies
materials
manufacturers
(200-300
companies)
The supplier Pyramid

## Slide 22: Consequences for suppliers
Suppliers located near the JIT-partner are in an advantageous position
Business based on open calculation
‘Quality on Time’
Supplier classification:
On time delivery | Quality delivery
A= excellent B=good C= inadequate | 1= excellent 2= good 3= inadequate
Example: C1 supplier provides high quality but does not always deliver on time
JIT and supplier selection

## Slide 23: Scheduling problems between purchasing and logistics
Some typical problem situations between purchasing and
logistics:
  Lack of well defined specifications
  Lack of standardization
  Frequent changes in materials planning
  Unreliable planning information
  Insufficient integration of purchasing in materials management

## Slide 24: Elements of the purchasing system
Most important elements of a purchasing system:
  Requisitioning and ordering
  Product, supplier and contract database
  Order follow up
  Delivery
  Invoice handling and payment

## Slide 25
Non-acceptance:
return to supplier
Incoming inspection
and quality control
Invoice
processing
Supplier
evaluation
Order monitoring and
expediting
Order processing
Quotation
Supplier selection
Purchasing
requirements
Article file
Supplier file
Contract file
Major elements of the purchasing system